REPORT SIGNAL GENERATOR
The generateTestSignal.m file, as the name suggests, deals with the generation of the signals that will be used later to test both tracking and acquisition scripts of the simulator. The signals that it allows to generate are heterogenous, and each of them has its parameters handled by a struct whose fields are:
name: name of the binary file where the generated signal will be saved.
dstart: starting doppler frequency.
dend: last doppler frequency.
deveryChip: boolean variabile, if set to true the doppler increment (or decrement) will be added every chip period, otherwise it will be added every symbol period.
dmode: available modes are {1=linear,2=triangular,3=cosine,4=quadratic}, and each of them specifies a different doppler behavior (for further details see section doppler behaviors).
envelope: set to 1 to add the sinusoidal envelope caused by the doppler on top of the signal.
inNoise: N0 parameter of the Gaussian Noise added to the information signal.
envelopePhase: phase (in radiant) of the sinusoidal envelope.

outNoise_Length: number of pure noise samples added before and after the useful signal.

outNoise: N0 parameter of the Gaussian pure noise samples.

outBits_Length: number of random bits to be added at the beginning and at the end of the packet, before the multiplication by the PRN.

outPRN_Length: number of PRN bits (max=4092) to be added in front and after the multiplication by the PRN.

powerReduce: exponent of the signal’s amplitude attenuation, if set to 3 (as an example) the signal will be reduced by 2^3=8 times with respect to the signal’s maximum amplitude.

Doppler Behavior

Since the satellite is not “moon-synchronous”, its speed seen by the receiver fixed on the moon’s surface is changing. This change will cause a varying Doppler since fd = 2*f0*relative_velocity/c. With this in mind, we have decided to generate signals with different doppler behaviors resumed as follow:

Graphs of LINEAR-QUADRATIC-…

Signal Generation

The doppler causes not only the presence of a sinusoidal envelope that the down conversion at the nominal frequency isn’t able to resolve, but also the shrinking/stretching of the symbol’s period. We took this effect into account, generating symbols whose duration is variable according to the doppler they experience. Since the sampling frequency is fixed, a reduction of the symbol time (caused by a positive doppler) will result in a lower number of samples available of that symbol (for a negative doppler we have the opposite effect).

Graphs of different duration of the symbols according to doppler